## Slide 1: power electronics
Semi Controlled Rectifier
Presentation on
Presented By:
Amanjeet Kumar ( BT18EE011 )

## Slide 2: Topics to be cover :
Introduction
Silicon Controlled rectifier (SCR)
Static V-I Characteristics of SCR
Protection of SCR

## Slide 3: Introduction
The name ‘Thyristor’ is derived by a combination of the capital letters from THYRatron and transistor.
International Electrotechnical Commission (IEC) in 1963 decided the definition of thyristor as under :
  It constitutes three or more p-n junctions.
  It has two stable states, an ON-state and can change its state from one to another.
Thyristor is a four layer, three-junction, p-n-p-n semiconductor device.

## Slide 4: Silicon Controlled Rectifier (SCR)
SCR is the oldest at first member of thyristor family.
It is called SCR because silicon is used for its construction and its operation as a rectifier very low resistance in forward conduction and very high resistance in the reverse direction can be controlled.
It has three terminals
  Anode(A)
  Cathode(K)
  Gate(G)

## Slide 5
The structure of SCR
  The terminal connected to outer ‘p’ region is called anode.
  The terminal connected to outer ‘n’ reason is called cathode.
  The terminal connected to inner ‘p’ region is called the gate.
SCR is a unidirectional device. It blocks the current flow from cathode to anode.

## Slide 6: Static V-I Characteristics of SCR
An elementary circuit diagram for obtaining static V-I characteristics of SCR is shown in figure,
The anode and cathode are connected to main source through the load.

## Slide 7
The static V-I characteristics of SCR are shown below,
The three basic modes of operation of SCR are,
  Forward blocking mode
  Forward conduction mode
  Reverse blocking mode
Va = Anode Voltage
Ia = Anode Current
VBO = Forward Breakover Voltage
VBR = Reverse Breakdown Voltage
Ig = Gate Current
IL = Latching Current
IH = Holding Current

## Slide 8
Forward blocking mode:
  When anode is at higher potential than cathode, with gate circuit open, thyristor is said to be forward biased.
  It is seen from the figure that J1, J3 are forward bias but junction J2 is reverse bias.
  In this mode a small current called forward leakage current flows from anode to cathode.
  OM in the V-I characteristics represents the forward blocking mode of SCR.
  SCR is treated as an open switch in the forward blocking mode.
Figure : Forward blocking mode of SCR

## Slide 9
2. Forward conduction mode:
  When anode to cathode forward voltage is increased with gate circuit open reverse biased junction J2 will have an avalanche breakdown voltage called forward breakover voltage VBO.
  After this breakdown, thyristor gets turned on with point M at once shifting to N. Here NK represents the forward conduction mode.
  Thyristor can be bought from forward blocking mode to forward conducting mode by turning it on by applying.
    A positive gate pulse between gate and cathode (or)
    A forward breakover voltage VBO across anode and cathode.
  Voltage drop across the SCR, VT increases slightly with an increase in anode current. it can be seen from NK.
  Latching current(IL):
    It is defined as the minimum value of anode current Ia which it must attend during turn on process to maintain conduction when gate signal is removed.
    The gate pulse width should be chosen to ensure that the anode current Ia just above the latching current IL.

## Slide 10
Holding current (IH):
  It is defined as the minimum value of anode current below which it must fall for turning off the SCR.
  Letting current IL is more than holding current IH.
      i.e. IL > IH
  Letting current is associated with turn on process.
  Holding current is associated with turn off process
Reverse blocking mode :
  When cathode is made high potential with respect to anode with gate open, then the SCR said to be reverse biased.
  J1 and J3 are reverse biased and J2 is forward biased.
  Small current flows through the SCR this is called as reverse leakage current.
  This is reverse blocking mode called the off state of the SCR.
  If the reverse voltage is increased then at reverse breakdown voltage and avalanche occurs at J1 and J3 and the reverse current increases rapidly.(PQ)
  The SCR in the reverse blocking mode may therefore be treated as an open switch.

## Slide 11
Figure – Reverse Blocking Mode of SCR

## Slide 12
Gate characteristics of SCR
Trigger circuit connected to gate cathode circuit of an SCR.

## Slide 13: Forward Gate characteristics of SCR

## Slide 14
Vg, Ig characteristics has spread between two curves 1 and 2 as shown in figure.
Curve and corresponds to get with maximum doping. So it requires lowest voltage values that must be applied to turn on the SCR.
Curve 2 corresponds to gate with minimum doping. So it requires highest possible voltage values that can be safely applied to gate circuit.
Each SCR has maximum limit as Vgm for gate voltage and Igm for gate current. There is also average gate power dissipation Pgav specified for each SCR.
Vgm and Igm are the minimum limits for GATE voltage and gate current for turn on of SCR.
The above figures show that the preferred gate drive area for an SCR is ‘bcdefghb’.
For selecting the operating point of the circuit load line is drawn from A to D. Where as,
  Es = Gate Source Voltage = OA
  OD = Trigger Circuit Short Circuit Current =[Es/Rs]

## Slide 15
  Curve 3 gives the operating point ‘S’. Thus for this SCR,
  Gate voltage = PS
  and
  Gate Current = OP
Operating point s which may change from S1 to S2 and must lie within the limit curves 1 and 2 and must be as close to the curve as possible.
The minimum value of gate source series resistance r is obtained by drawing a line AC tangent to Pgav curve.

## Slide 16: Protection of SCR
  di/dt protection
    When a thyristor is forward biased and is turned on by gate pulse conduction of anode current begins. If the rate of rise of anode current is very fast compared with the spreading velocity of a turn on process local hot spots will be formed. This localised heating may destroy the thyristor. Therefore the rate of rise of a note current at the time of turn on must be kept below the specified limiting value.
    By using a small inductor called di/dt inductor in series with the anode circuit.

## Slide 17
  dv/dt protection
    If the rate of rise of suddenly applied voltage across the resistor is hard the device get turned-on. Such phenomena of turning on a thyristor called dv/dt turn on must be avoided as it leads to false operation.
    False turn on of a SCR by large dv/dt, even without application of gate signal can be prevented by using a Snubber circuit in parallel with the device.
    A Snubber circuit consists of a series combination of resistance and capacitance in parallel with the thyristor as shown in figure.
    Design of Snubber circuit
Figure - Snubber circuit across SCR

## Slide 18
When switch s is closed a sudden voltage appears across the circuit. Capacitor Cs behaves like a short circuit, therefore voltage across SCR is zero. With the passage of time voltage across Cs builds up at a slower rate such that the dv/dt across Cs and therefore across SCR is less than the specified maximum dv/dt rating of the device.
In order to limit their magnitude of discharge current a resistance Rs is inserted in series with Cs.

## Slide 19
Over voltage protection
  A SCR may be subjected to internal or external over voltages.
  Internal over voltages
  Due to the presence of the series inductance Ls of the the SCR circuit large transient voltage is produced and this internal voltage maybe e several times the break over voltage off the SCR the thyristor may be destroyed permanently.
  External over voltages
    Over voltages are caused due to the lightning strokes and switching surges.
    For reliable operation the over voltages must be suppressed by adapting voltage clamping device (v.c).
    A voltage clamping device is a nonlinear resistor connected across SCR figure. The voltage clamping device has following resistance characteristics with increasing voltage. Under normal conditions the device has a high resistance and drought only a small leakage current. When a voltage surge appears the voltage clamping device operate in low resistance region and produces is short circuit across SCR after the surge is treated IT returns to normal high resistance.

## Slide 21: Over Current Protection
If a SCR is subjected to overcurrent due to faults, short circuit (or) surge current, its junction temperature may exceed the rated value and the device may be damaged.
There is a need for the overcurrent protection of SCR.
  Fast acting current limiting fuse(FACLF)
  Circuit breakers are used.
Gate Protection
Over voltages and over currents across the grid circuit can cause false triggering of the SCR.
Protection against over voltages is achieved by connecting a zener diode ZD across the gate circuit.
Protection against the overcurrent is achieved by connecting a transistor R2 in series with gate circuit.
A capacitor and a resister and also connected across Kittu cathode to bypass the noise signals.

## Slide 22: Circuit Components Showing The Thyristor Protection
Thermal protection
If temperature increases installation is weakened, resulting in leakage currents which interference with operation. Heat sinks which include aluminium disk are used along with ventilating ducts, increased surface area coolants are used.